## Slide 1
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu
Video Links
https://youtu.be/7QhV2R64oDM
https://github.com/txoritxo/cs231a_Project/blob/main/presentation/cs231a_project_full.mp4

## Slide 2
Problem Statement
UAVs need to be able to navigate with onboard cameras.
Accurate navigation is very sensitive to a good calibration though.
Temperature fluctuations, vibrations, zoom functionalities, etc. all can make a laboratory calibration invalid
Autocalibration in flight is a solution, yet at altitude, scene is mostly planar, making traditional methods inapplicable
Need to take advantage of the scene structure!
[Triggs ’98] first presented a method specifically dedicated to planar scenes based upon inter-image homographies
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu

## Slide 3
Technical Approach
Feature Extraction
& Matching
Step 1
SIFT feature extraction
FLANN matching
Filtering
Projective
Reconstruction
Step 2
Homography estimation
RANSAC
Projective
Bundle Adjustment
Step 3
Initial estimation of distortion and Central Point
Refinement of Homographies and world coordinates of scene points
Assumptions
Asm.
Planar scene
Camera
  zero-skew
  Radial distortion model
“Forget the checkerboard: practical self-calibration using a planar scene”
Herrera et. Al, WACV 2016
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu

## Slide 4
Step 4
Metric Reconstruction
Step 5
Metric
Bundle Adjustment
Step 6
Technical Approach
Focal length estimation
Non-linear minimization
Principal point correction
Initial extrinsic guess for reference frame
Approximate 3D point coordinates in reference frame (triangulation)
Extrinsic parameters for all frames using PnP
Minimization of reprojection errors
Refine 3D scene point coordinates
Refine intrinsics and distortion
Homography based
Self-Calibration
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu

## Slide 5
Results – Close Range Imagery
Baseline calibration
DSLR + 18mm lenses
Baseline: Checkerboard calibration
Resized to 800x533 px
 |  | Checkerboard Cal. | Planar Self-Cal. | Deviation( %)
Focal Length | fx | 657.611 (18.25 mm) | 664.954 (18.45 mm) | 1.12
 | fy | 658.268 (18.27 mm) | 666.036 (18.49 mm) | 1.18
Principal Point | u | 401.66 | 425.684 | 5.98
 | v | 289.896 | 283.173 | 2.32
Distortion | d0 | -1.76E-01 | 3.75E-07 | 100.00
 | d1 | 1.04E-01 | 3.96E-13 | 100.00
Pixel Error |  | 0.65 | 0.58 | 10.28
Matlab Calibration Toolbox
Custom planar self calibration method
Results
Focal Length very accurate ~ 1.2%
Less accurate Principal point ~ 2.5–6 %
Reprojection error slightly better than Checkerboard
High error in distortion, probably due to different Distortion models
Planar self-calibration: Poster Pictures
Custom Python implementation
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu

## Slide 6
Results on real aerial imagery
 | Autocalibration | Ground Truth | Error [%]
 | 1766.25 px | 1749.42 px | 0.94
 | 1765.00 px | 1747.92 px | 0.98
 | 1916.59 px | 1891.50 px | 1.3
 | 1085.18 px | 1085.92 px | -0.07
 | -0.206 | -0.268 | 23.1
 | 0.0001 | 0.011 | -
 | Autocalibration | Ground Truth | Error [%]
 | 1766.25 px | 1749.42 px | 0.94
 | 1765.00 px | 1747.92 px | 0.98
 | 1916.59 px | 1891.50 px | 1.3
 | 1085.18 px | 1085.92 px | -0.07
 | -0.206 | -0.268 | 23.1
 | 0.0001 | 0.011 | -
Real flight imagery from landing maneuver at Sanderson Field Airport (Washington).
4K resolution images taken with GoPro camera (forward-looking).
Real lenses with radial + tangential distortion.
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu

## Slide 7
Results – Satellite Imagery
osgEarth is used to transform satellite orthoimagery to a given virtual camera perspective
 |  | Specified Cal. | Planar Self-Cal. | Deviation( %)
Focal Length | fx | 1117.65 | 1527.25 | 36.7
 | fy | 1117.65 | 1455.30 | 30.3
Principal Point | u | 511.5 | 480.65 | 6.0
 | v | 383.5 | 415.15 | 8.3
Distortion | d0 | 0 | -3.29E-09 | -
 | d1 | 0 | -1.2515E-14 | -
Pixel Error |  | N/A | 0.07 | -
Poor results
Large estimation errors even though plane is performing roll maneuver in sample images, i.e. rotation + translation.
Measures to improve numerical conditioning for optimization:
normalized feature points, program Jacobians for bundle adjustments, select homographies with best condition numbers
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu

## Slide 8
Conclusions
Close-range imagery results: Promising results with checkerboard in comparison with standard methods. Distortion model fitting plays important role.
[Herrera ’16] Autocalibration fully implemented in Python
Runway imagery results: Very promising results with real flight imagery in special landing case. Good use case!
Need to further take advantage of the scene structure to get yet better results for this application.
[Yang ’19] presented a method specifically dedicated to autocalibrate planar scenes with pure translational movement
High altitude imagery results: Suspect too close to degenerate case of pure translation between views of planar imagery.
Real flight imagery with perpendicular view
mpalomar@stanford.edu
carlosq@stanford.edu
mwhardt@stanford.edu